 A CLOSER LOOK AT KECCAK
- Keccak Basics
  - Parameters
  - Sponge Function
- Internal Structure
  - Padding
  - F-functions
- Security and Performance Analysis

---
 PARAMETERS
- All SHA-3 functions are governed by 4 main parameters:
  - Output bits—the length of the message digest: 224, 256, 384, and 512
  - b—buswidth, b=25*2^l where 2^l is the width of a processor’s register
    - For SHA-3 this is fixed for a 64-bit processor b=1600 bits
  - r—rate (defines the speed)
  - c—capacity (defines the security)
https://keccak.team/keccak_specs_summary.html

---
 PARAMETERS
https://keccak.team/keccak_specs_summary.html

---
 SPONGE FUNCTION
SHA-3 HASH
Stops here
https://nvlpubs.nist.gov/nistpubs/FIPS/NIST.FIPS.202.pdf

---
 INTERNAL STRUCTURE: PADDING
- Main goal of padding is to make sure message is divisible by r
- Here, the length of the padding is:
  r/8-M/8 mod (r/8), where M is length of the message
https://keccak.team/keccak_specs_summary.html
https://nvlpubs.nist.gov/nistpubs/FIPS/NIST.FIPS.202.pdf

---
EXAMPLE
- Let’s say we’re taking the hash of a 1kB file using SHA-3 256:
- B=1600, r=1088, c=512
  - We start with 1600 bits of zeros and xor the first 1088 bits of the padded message
- Padded M is 1kB plus padding (88B) or 8704 bits
  - So we absorb 8 times for each chunk of the padded message
- After the last absorption, we rip off the first 1088 bits, and truncate to 256 bits (64 characters)

---
 INTERNAL STRUCTURE: F-FUNCTIONS
- Consists of 5 functions that each run for 24 rounds:
  - Theta (θ)
  - Pi (π)
  - Rho (ρ)
  - Chi (χ)
  - Iota (ι)
- These functions operate by organizing the input block into a 3-d array 5x5x64
http://www.crypto-textbook.com/
https://github.com/XKCP/XKCP/blob/master/Standalone/CompactFIPS202/Python/CompactFIPS202.py

---
 INTERNAL STRUCTURE: F-FUNCTIONS
- Theta (θ): takes the XOR sum of 11 bits

---
 INTERNAL STRUCTURE: F-FUNCTIONS
- Rho (ρ) and Pi (π)
  - ρ bit rotates each of the 64-bit lanes by a fixed amount
  - π permutes these lanes with others

---
 INTERNAL STRUCTURE: F-FUNCTIONS
- Chi (χ)
  - take lane [x+2,y] AND inverse of lane [x+1, y]
  - XOR this result with lane (x,y)

---
 INTERNAL STRUCTURE: F-FUNCTIONS
- Iota (ι)
  - Simply add a bit constant to the first lane:
    - A[0,0] =A[0,0]⊕RC[i]

---
SECURITY AND PERFORMANCE
https://en.wikipedia.org/wiki/SHA-3

---
MORE INFO
- The author of our textbook has published an excellently detailed lecture on this algorithm!
  - (you might pick up some German too)
  https://www.youtube.com/watch?v=JWskjzgiIa4
- If you want to check out other uses for Keccak other than hashing see:
  - https://nvlpubs.nist.gov/nistpubs/ir/2012/NIST.IR.7896.pdf
  - https://keccak.team/files/SpongeDuplex.pdf
  - https://en.wikipedia.org/wiki/Authenticated_encryption
  - https://www.youtube.com/watch?v=wgR3VYHdd4Y